## Slide 1: Networks – Network Fundamentals

## Slide 2: How do computers connect to each other?
Wired vs. Wireless
Network cards
  Special device on computer that lets the computer connect to a network
  Can be wired or wireless
Switches
  Centralized device connecting multiple computers
Routers
  Forwards (routes) packets of data to the appropriate destination

## Slide 3: Network Hardware

## Slide 4: Standards & Protocols
Standard – a common language
  Standards enable compatibility through a common “language” internationally
Protocol - agreed set of rules (how to do something)
Why are these important?
Examples:
  HyperText Transfer Protocol (HTTP)
  Internet Message Access Protocol (IMAP)
  Internet Protocol (IP)
  Transmission Control Protocol (TCP)

## Slide 5: Circuit-switched vs. Packet-switched Networks
Circuit-switched Network Example: Phone Network
  http://www.tcpipguide.com/free/t_CircuitSwitchingandPacketSwitchingNetworks.htm
  http://en.wikipedia.org/wiki/File:Photograph_of_Women_Working_at_a_Bell_System_Telephone_Switchboard_(3660047829).jpg
What are the problems with circuit-switched networks?
Packet-switched Network Example: The Internet
  http://vimeo.com/10347883

## Slide 6: Packet Switching
Break data up into packets & transmit
Individual packets are not all necessarily transmitted through the same links
Each packet travels over the best available link at the time
Packets may arrive at destination out of order  must be re-ordered and reassembled

## Slide 7: Data Packets
  envelope of data sent between computers
  typically contains:
  source (origin) address
  destination address
  sequence numbers (for packets that combine into one larger piece of data)
  timestamp (i.e. postmark)

## Slide 8: Network Layers
Network communication broken up into layers
Each layer worries about something specific
Open Systems Interconnection (OSI) model
  Layer 7: Application (e.g. web browser)
  Layer 6: Presentation
  Layer 5: Session
  Layer 4: Transport
  Layer 3: Network
  Layer 2: Data link
  Layer 1: Physical (e.g. network cable)

## Slide 9: Local Area Network (LAN)
Computers connected together in a geographically local area
Examples:
  A computer lab
  Your home’s network

## Slide 10: Virtual Local Area Network (VLAN)
Computers grouped together or mutually isolated to mimic a LAN, but are not geographically local
  They do not have to be connected all to the same centralized device (e.g. switch, router)

## Slide 11: VLAN Example

## Slide 12: Wireless Local Area Network (WLAN)
LAN where computers are connected wirelessly
Example:
  Washington-Lee’s wifi
  Your home’s wifi

## Slide 13: Wide Area Network (WAN)
a really, really big network
  your house  ISP  Internet
  Washington-Lee  Yorktown  etc.
allows a computer to connect to other computers over a wide geographic area

## Slide 14: Storage Area Network (SAN)
Network that provides data storage
Examples:
  Data centers
  Cloud storage

## Slide 15: Virtual Private Network (VPN)
Extends a private network across a public network (e.g. Internet)
You create a VPN connection/tunnel from your computer to the private network
Private networks try to remain private, so VPN connections are encrypted
Example:
  http://en.wikipedia.org/wiki/File:Virtual_Private_Network_overview.svg

## Slide 16: VPN Example

## Slide 17: What do you need for a VPN?
Two endpoints
Authentication protocol– verifying the identity of each end point
Connection protocol(s) to connect the two endpoints and create the VPN tunnel
Encryption protocol to secure the tunnel (i.e. Nobody can read the packets in the tunnel)

## Slide 18: Evaluate the use of VPNs
Benefits?
Costs?

## Slide 19: Personal Area Network (PAN)
Connected devices in an individual’s area
Most popular protocol: Bluetooth
Examples:
  Phone <-> speaker
  Phone <-> car
  Phone <-> earpiece

## Slide 20: Client-Server Model
Centralized model where clients connect to a server
server
  provides services to the network
client
  requests actions from a server (i.e. makes requests to a server)
Example:
  Websites
  Napster

## Slide 21: Peer-to-Peer (P2P)
Decentralized
All computers connected act as both clients and servers
Everybody acts as a consumer and a supplier
Example:
  Bittorrent

## Slide 22: Internet
All computers on the Internet have a unique IP address
  Regulated internationally by Internet Assigned Numbers Authority (IANA)
Domain names (www.DOMAINNAME.COM)
  Regulated by Internet Corporation for Assigned Names and Numbers (ICANN)
How do you connect to a website on the internet?
  You NEED the IP address!

## Slide 23: Why did the Internet grow so quickly?
Moore’s Law
  # of transistors on integrated circuit doubles about every two years
  Exponential growth of power
  Exponential decay of cost
  Examples:
    CPUs
    Flash drives
Metcalfe’s Law
  Usefulness of a network ~ n^2
  n(n − 1)/2  n^2