## Slide 1: Introduction to Networking

## Slide 2: Key Terms
packet
  envelope of data sent between computers
server
  provides services to the network
client
  requests actions from a server (i.e. makes requests to a server)

## Slide 3: Local Area Network (LAN)
computers and peripherals directly linked together in a single area
  room, office, or building
enables sharing of peripherals (e.g. printer)
commonly uses client-server model
  one machine acts as the central node (server)
  all others are clients
LANs may connect to other LANs or to the outside using a “gateway”

## Slide 4: Wide Area Network (WAN)
a really, really big network
  your house  ISP  Internet
  Washington-Lee  Yorktown  etc.
allows a computer to connect to other computers over a wide geographic area

## Slide 5: Hardware
network cable
Network Interface Card (NIC)
hub
  connects together multiple computers or segments
  any incoming data will be broadcasted out to all ports
switch
  connects together multiple computers or segments
  analyzes network traffic and learns which machines are connected to particular ports
  incoming data is forwarded through proper port
router
  forwards traffic to proper destination
  programmable (e.g. filter traffic)
gateway
  a computer that connects users of a LAN to another network

## Slide 6: Types of Network Cables
Modes of communication
  Telephone lines ~ dialup
  Coaxial cable ~ cable internet
  Twisted pair ~ ethernet
  Fiber-optic ~ FIOS
  Microwave (high frequency radio) ~ wifi
  Satellite

## Slide 7: Packets
an envelope of data sent between computers
typically contains:
  source (origin) address
  destination address
  sequence numbers (for packets that combine into one larger piece of data)
  timestamp (i.e. postmark)

## Slide 8: Packet-switched vs. Circuit-switched Networks
http://vimeo.com/10347883

## Slide 9: Packet Switching
Break data up into packets & transmit
Individual packets are not all necessarily transmitted through the same links
Each packet travels over the best available link at the time
Packets may arrive at destination out of order  must be re-ordered and reassembled (protocol!)